Shotclock design choices / notes

A product that displays a countdown timer on seven segment displays once a button has been pressed. The countdown will show a maximum of 99 seconds (2 digits), and each of these 2 digits should be present on 4 sides of the product (so a total of 8 seven segment displays).
A buzzer is added to audibily hear when the timer has ran out.
See requirements below for more info.
# Requirements
1. Battery powered, rechargable
1.1 Li-Po would be nice, since large capacity and shitload of form factors
1.2 USB type C connector as charge plug (charging may stop usage of product if using li-po)
1.3 USB type C connector as USB D+/D- to MCU
2. Can drive 2x4 seven segment displays, with brightness control
3. LED to display battery < 20%
4. LED to display charging status (is charging and is done charging)
5. Switch (latching) to turn product on and off, while still being able to charge product (preferably in both the on and off state. But only off state is also fine for version 1).
6. Three functional buttons (momentary) with hardware debouncing
7. STM32 MCU, with SWD connector
8. UART header
9. Bootloader button to STM
10. Buzzer to indicate that the timer has ran out.
11. EEPROM to store user settings (atleast countdown time and buzzer on/off).

# Battery charger & ADC charge status
TP4056 as charging IC (https://dlnmh9ip6v2uc.cloudfront.net/datasheets/Prototyping/TP4056.pdf)
Page used on deciding charge current:
https://www.xtar.cc/news/What-Is-The-Best-Charging-Current-And-How-To-Calculate-The-Charging-Time-Of-Lithium-Battery-154.html
Disable system while charging battery:
https://www.microtype.io/lithium-ion-battery-charger-circuit-load-sharing/
Choosing battery of 1500 or 2000 mAh, since it is good middle-way between size, weight, price and capacity (should last the product more than long enough to be able to only charge it when systemload is off).
I got these in house: https://nl.aliexpress.com/i/1005005148897780.html?gatewayAdapt=glo2nld
With a thermistor in them. Still need to calculate R1 and R2 for the TP4056, by measureing ambient room temperature and measuring the thermistors resistance (used this article: https://www.best-microcontroller-projects.com/tp4056-page2.html)
3 pin JST connector:
https://jlcpcb.com/partdetail/171769-BM03B_SRSS_TB_LF_SN/C160389
Might also want to add a 2 pin JST connector, since a lot of li-ion cells don’t have a thermistor in them.
To read the amount of charge in the battery, I want to use the ADC of the STM32.
This article was used as example: https://vivonomicon.com/2019/10/15/reading-battery-voltage-with-the-stm32s-adc/
It mentions that: “if you use smaller resistor values for the voltage divider, you use more current, but the sampling can be faster”. A commentor on that post replied: “You can use larger resistors (i.e. 1M) in the divider and still use short sampling times if you add a small capacitor (1n-100n). [between the Analog pin and ground, to buffer so the ADC peripheral gets current more quickly. Instead of via the high resistance path of the voltage divider]”.
So that is what is implemented. A 1:1 voltage division (a single Lithium cell get to a max of 4.2V, so divided by 2 will give a max of 2.1V, which the analog pins easily accept), with large resistance values (1M) and a 100n capacitor between the analog ADC peripheral and GND.
Current leakage would be:
4.2 = I * 2000000
I = 0.0000021 amps (or 2.1 microamps).
Should be reasonable for a 1500mAh battery (or is it smart to increase the resistance values & capacitor value even more, to reduce the current leakage even more?).

And for the battery level status led:
Assuming a forward voltage drop of 2.0 volts and a forward current of 10 mA, we can calculate the resistor value using Ohm's Law (V = IR). Rearranging the formula, we get R = V / I.
R = (Vsupply - Vf) / I
R = (3.3V - 2.0V) / 0.01A
R = +/- 130 Ω (130 is closest std. value.)
# Voltage regulator (3v3)
TPS63000, variable output DC/DC buck boost.
Variable output calculation
From datasheet:
8.2.2 Detailed Design Procedure
8.2.2.1 Programming the Output Voltage
Within the TPS6300x family, there are fixed and adjustable output voltage versions available. To properly configure the fixed output voltage devices, the FB pin is used to sense the output voltage. This means that it must be connected directly to VOUT. At the adjustable output voltage versions, an external resistor divider is used to adjust the output voltage. The resistor divider must be connected between VOUT, FB and GND. When the output voltage is regulated properly, the typical value of the voltage at the FB pin is 500 mV. The maximum recommended value for the output voltage is 5.5 V. The current through the resistive divider should be about 100 times greater than the current into the FB pin. The typical current into the FB pin is 0.01 μA, and the voltage across the resistor between FB and GND, R2 , is typically 500 mV. Based on those two values, the recommended value for R2 should be lower than 500 kΩ, in order to set the divider current at 1 μA or higher. TI recommends to keep the value for this resistor in the range of 200 kΩ. From that, the value of the resistor connected between VOUT and FB, R1 , depending on the needed output voltage (VOUT), can be calculated using Equation 1. (1) If as an example, an output voltage of 3.3 V is needed, a 1-MΩ resistor should be chosen for R1 . To improve control performance using a feedforward capacitor in parallel to R1 is recommended. The value for the feedforward capacitor can be calculated using Equation 2.

## R2 calculation
Wanted Vout is 3v3.
R1 = 1M (according to datasheet 8.2.2.1)
R2 = ?
Vout = 3.3V
Vfb = 0.5V (typical value from datasheet 8.2.2.1)

Solving for R2:
R2 = (Vfb * R1) / (Vout - Vfb )
R2 = (0.5 * 1000000) / (3.3 – 0.5) = 178571,4285714286 ohms.

Solved for Vout (to make sure I did not make a solving mistake):
Vout = (Vfb * (R1 + R2) ) / R2
Vout = (0.5 * (1000000 + 178000)) / 178000 = 3,308988764044944 = 3.3v.

So chosen R2 = 178k.

## Cff calculation
2.2us = 0.0000022 s
R1 = 1000000 ohm
Cff = 2.2us / R1 = 0.0000022 / 1000000 = 0.0000000000022 F
0.0000000000022 F = 2.2 pF
So Cff should be 2.2pF

# Momentary buttons and hardware debouncing
I want 3 digital input momentary buttons, with hardware debouncing integrated into the PCB.
Schmitt Trigger IC chosen for debouncing: STM m74hc14yrm13tr.
Because the internet said this IC is great for button removing hysterisis at 3v3 levels since it is a really fast schmitt trigger IC. The IC doesn’t need additional configuration. Also the IC is ok in terms of availability.
https://www.st.com/resource/en/datasheet/m74hc14.pdf
I’ve used ‘snapeda.com’ to create a schematic symbol (footprint was already available). Quite useful stuff: https://www.snapeda.com/parts/M74HC14YRM13TR/STMicroelectronics/view-part/

# Buzzer
To make sure the buzzer does not pull to much current from the MCU, an NPN transistor is used:
Also a flyback diode is placed between buzzer pins, to act as a bypass if the magnetic field collapses, to not damage the transistor.
A current limiting resistor of 1k ohm is used for the base pin of the transistor.
Then 3v3 is connected to GND, via the transistor.

# Connectors to seven (eight) segment displays
The used segment displays are common cathode: https://t.ly/1rQHq (short URL, because AliExpress creates huge URLs).
There are 8 segments (7 for the digit, 1 for a dot), and two ground pins per display:

PIN 1 = GROUND
PIN 5 = GROUND
PIN 2 = E
PIN 3 = D
PIN 4 = C
PIN 6 = B
PIN 7 = A
PIN 8 = DP
PIN 9 = F
PIN 10 = G

The displays will be mounted on seperate PCB’s for easy product assembly (the displays have pins, so the PCB’s will have header sockets). Then, each segment PCB will be connected to the main shotclock PCB, also using header pins/sockets.

To minimize noise, low impedance paths and reduces the chances of ground bounce or voltage fluctuations, I’ll try to add as much ground pins between the two PCB’s as possible.

Each segment PCB will mount two segment displays (each display should be able to show a different digit). Each shotclock will have 4 segment PCB’s mounted in 90° offset rotation from main PCB center. These all show the same 2 sets of digits (hense, 16 signals needed in total). The transistors will be mounted on the segment display PCB, not on the main PCB. Main PCB will only provide power, GND & PWM signals.

Since there are 16 (PWM) signal lines needed between the boards, I’ll try and fit 16 ground pins, together with 16 signal pins, and 1 3v3 pin between each PCB. This comes to a total of 33 connections between the boards.

When using 2.54mm pitch header pins/sockets, the physical space needed for each connector is:
2.54 * 33 = 83,82mm, which should easily fit in a one row setup. The chosen segment displays are 40mm wide per display, so the product must be and will be atleast 100mm wide.

If 1x33 header pins/sockets are difficult to source, I could also use 2 rows, which would mean they would be 83,82mm/2 = 41,91mm wide. For now, I’ll just use one row of 33 pins.

# Thoughts and questions
1. Should I connect Vbat of the MCU? I believe it is used to power the internal RTC right? Could be handy maybe? And where would be logical to connect it (so that it is always on, also when charging)?
2. Is it smart to add reverse polarity protections, or ESD protections? If so, where?
3. Any handy places to put a test point, that I have forgotten?